## Slide 1: Flow Scheduling for Interactive Video Streaming
MD Iftakharul Islam (Tamim)
Department of Computer Science
Kent State University
Kent, OH, USA.

## Slide 2: Outline
Problem scope
Maximum-weight Independent Set
Graph construction (interval graph)
Flow Scheduling

## Slide 3: Logical Architecture of a Router

## Slide 4: Competing Flows
IP routers provide differentiated services
  Different types of traffics are allocated with different resources, so web traffic and video streaming don’t compete with each other.
  Video streaming flows compete among themselves for the allocated resources.
Router
Outgoing channels
s1
s2
s3
s4
s5
Video streaming sources

## Slide 5: Video Streaming
A source sends a video in a regular interval (Usually several times in a second)
Though the duration of each video is same, their size varies
  Achieving constant quality results in Variable Bit Rate (VBR).
    High motion scene needs more bits than little motion
    High frequency scene needs more bit
Time
Video size (B)

## Slide 6: Packets in Time Unit
  Routers treat the video packets in an unit of time.
    Different routers have different processing power. So, size in bit is not universal across routers, but time does.
Time
Video size (B)
5
10
5
15
12
time

## Slide 7: Competing Flows
How to schedule the flows to a channel (port) such that the channel utilization is maximized?
5
10
5
15
12
5
5
15
12
5
10
5
15
12
time
Flow 1
Flow 2
Flow 3
Router’s Output Buffer

## Slide 8: A possible solution
Does it maximize the channel utilization? - NO
5
10
5
15
12
5
5
15
12
5
10
5
15
12
time
Flow 1
Flow 2
Flow 3
Router’s Output Buffer

## Slide 9: Candidate Solutions
Greedy Strategy? Earliest Deadline First?
  Suboptimal result (Will pick B over J)
0-1 Knapsack problem?
  NP-complete. Dynamic programming based pseudo polynomial time algorithm exists.
Maximum-weight independent set of a graph
B
A
C
E
D
F
G
I
H
K
J
L
N
M
time
Flow 1
Flow 2
Flow 3
Router’s Output Buffer

## Slide 10: Graph Construction
C
E
D
I
H
K
L
N
M
time
Flow 1
Flow 2
Flow 3
C
H
K
D
L
I
E
M
N
L
Nodes | Weight
C | 5
D | 15
E | 10
H | 8
I | 7
K | 5
L | 7
M | 8
N | 8

## Slide 11: Maximum-weight Independent Set (MWIS)
MWIS is an independent set whose weights sum is maximum.
NP-hard on general graph but O(n+m) for interval graph
C
H
K
D
L
I
E
M
N
Nodes | Weight
C | 5
D | 15
E | 10
H | 8
I | 7
K | 5
L | 7
M | 8
N | 8

## Slide 12: Maximum-weight Independent Set
Find the umbrella-free ordering. O(n+m)
Find the independent sets from the umbrella-free ordering.
Find the maximum-weight independent set from the IS.
Maximum Independent Set {C, L, M, N} = 28
Maximum-weighted Independent Set: {K, D, E} = 30
C
H
K
D
L
I
E
M
N
Nodes | Weight
C | 5
D | 15
E | 10
H | 8
I | 7
K | 5
L | 7
M | 8
N | 8

## Slide 13: Flow Scheduling
C
E
D
I
H
K
L
N
M
time
Flow 1
Flow 2
Flow 3
C
H
K
D
L
I
E
M
N
L

## Slide 14: References
Xiaojun Cao, Yichuan Wang, Alex Zelikovsky “Scheduling Bursts using Interval Graphs in Optical Burst witching Networks”, IEEE GLOBECOM 2009.

## Slide 15
Thank you!